Data Sheet  RFS-0827-20

Directional Coupler Specifications and Plots

Technical Specifications: 	(800-2700Mhz Directional Coupler but work well down to 600 MHz)

Model:                      			RFS-0827-20

Coupling(dB):            			20 ±1.1

Frequency(MHz):       			800-2700   (600 -2700)

Insertion Loss(Db):     		0.2dB  (This includes 0.1dB loss due to coupling)

Isolation(dB):             			≥20

VSWR:                     			≤1.25:1

Power Rating(w):        		200

Impedance (ohm):       		50

Temperature(deg C):     		-35 ~ +125

Connector:                 			N (fem)

Colour:                       			Grey

Size:                        			156*63*16.5

Plots: