Data Sheet  RFS-SCO12V3

Directional Coupler Specifications and Plots

Technical Specifications: 		(600-3000Mhz Directional Coupler)

Model:                      			SCOV12V3

Coupling(dB):            			13 ±1

Frequency(MHz):       			600-3000

Insertion Loss(Db):     		0.5dB  (This includes 0.25dB loss due to coupling)

Isolation(dB):             			≥20

VSWR:                     			≤1.25:1

Power Rating(w):        		80

Impedance (ohm):       		50

Temperature(deg C):     		-35 ~ +125

Connector:                 			N (fem)

Colour:                       	                       Aluminium (Alodyned)  <br>

Size                       			110 x 27 x27 exc connectors

Plots: